## Slide 1: Fundamental Simulation Concepts
Mohammad Ramshani
University of Tennessee

## Slide 2: What We’ll Do ...
Underlying ideas, methods, and issues in simulation
Software-independent (setting up for AnyLogic)
Example of a simple processing system
  Scope the problem
  Terminology
  Simulation by hand
  Some basic statistical issues
Spreadsheet simulation
  Simple static/dynamic models
Overview of a simulation study

## Slide 3: The System: A Simple Processing System
Arriving
Blank Parts
Departing
Finished Parts
Machine
(Server)
Queue (FIFO)
Part in Service
4
5
6
7
General intent:
  Estimate expected production
  Waiting time in queue, queue length, utilization of the machine (the proportion of time the machine is busy)
Time units
  Different units in different places … must declare
  Check units when specifying inputs
  Declare base time units for internal calculations, outputs
  Be reasonable (interpretation, roundoff error)

## Slide 4: Model Specifics
Initially (time 0) empty and idle
Base time units: minutes
Input data (assume given for now) in minutes:
Part Number Arrival Time Interarrival Time Service Time
1 0.00 1.73 2.90
2 1.73 1.35 1.76
3 3.08 0.71 3.39
4 3.79 0.62 4.52
5 4.41 14.28 4.46
6 18.69 0.70 4.36
7 19.39 15.52 2.07
8 34.91 3.15 3.36
9 38.06 1.76 2.37
10 39.82 1.00 5.38
11 40.82 . .
. . . .
. . . .
Stop when 20 minutes of (simulated) time have passed
Notes: Production within 20 minutes = 5 parts; / 5
Average Waiting Time in Queue = 2.49 mins /

## Slide 5: Goals of Study: Output Performance Measures
Total production of parts over run (P)
Average waiting time of parts in queue:
Maximum waiting time of parts in queue:
= no. of parts which left the queue
= waiting time in queue of part
Question:
  WQ1 =
  N >
1
?
?
1

## Slide 6: Goals of Study: Output Performance Measures (cont’d.)
Average number of parts in queue over time:
Maximum number of parts in queue:
Average and maximum total time in system (a.k.a. cycle time):
Q(t) = number of parts in queue
at time t
TSi = time in system of part i

## Slide 7: Goals of Study: Output Performance Measures (cont’d.)
Utilization of machine (proportion of time busy)
Such measures are referred to as Key Performance Indicators (KPIs)

## Slide 8: Analysis Options
Educated guessing
  Average interarrival time = 4.08 minutes
  Average service time = 3.46 minutes
  So (on average) parts are being processed faster than they arrive
    System has a chance of operating in a stable way in long run, i.e., might not “explode”
    If all interarrivals and service times were exactly at their mean, there would never be a queue
    But data clearly exhibit variability, so a queue could form
  If we’d had average interarrival < average service time, and this persisted, then queue would explode
  Truth — between these extremes
  Guessing has its limits …

## Slide 9: Analysis Options (cont’d.)
Queueing theory
  Requires additional assumptions about model
  Popular, simple model: M/M/1 queue
    Interarrival times ~ exponential (what is the distribution of arrival times?)
    Service times ~ exponential, indep. of interarrivals
    Must have E(service) < E(interarrival)
    Steady-state (long-run, forever)
    Exact analytic results; e.g., average waiting time in queue is
  Problems: validity, estimating means, time frame
  But it’s all about approximation!

## Slide 10: Poison Distribution
Often the arrival process of customers can be described by a Poisson process
  Poisson process is a pure birth process
  The number of arrivals N(t) in a finite interval of length t obeys the Poisson(λt) distribution
  The interarrival times are independent and obey the Exp(λ) distribution
Notes: 1- In an infinitesimal time interval dt there may occur only one arrival. This happens with the probability λdt independent of arrivals outside the interval.
2- Moreover, the number of arrivals N(t1, t2) and N(t3, t4) in non-overlapping intervals (t1 ≤ t2 ≤ t3 ≤ t4) are independent.

## Slide 11: Mechanistic Simulation
Individual operations (arrivals, service times) will occur exactly as in reality
Movements, changes occur at right “times,” in right order
Different pieces interact
Install “observers” to get output performance measures
Concrete, “brute-force” analysis approach
Nothing mysterious or subtle
  But a lot of details, bookkeeping
  Simulation software keeps track of things for you
Notes: Mechanistic: We can understand the system by studying it’s underlaying parts and their relations
Brute-force: you go through all possible scenarios and enumerate them.

## Slide 12: Pieces of a Simulation Model
Entities
  “Players” that move around, change status, affect and are affected by other entities
  Dynamic objects — created, processed, removed (maybe)
  Usually represent “real” objects/beings
    Examples: parts in a factory, pizza in a pizzeria, drinks in a bar
    Can have “fake” entities for modeling “tricks”
    Breakdown demon, break angel
      Though Arena has built-in ways to model these examples directly
  Usually have multiple realizations floating around
  Can have different types of entities concurrently
  Usually, identifying types of entities is first thing to do in building model

## Slide 13: Pieces of a Simulation Model (cont’d.)
Attributes
  Characteristic of all entities: describe, differentiate
  All entities have same attribute “slots” but different values for different entities, for example:
    Time of arrival
    Due date
    Priority
    Color
  Attribute value tied to a specific entity
  Like “local” (to entities) variables

## Slide 14: Pieces of a Simulation Model (cont’d.)
(Global) Variables
  Reflect characteristics of the whole model, not of specific entities, i.e.,
    Values for which there’s only one copy for whole model
  Example:
    Travel time between all station pairs
    Number of parts in system
    Simulation clock
  Not tied to entities
  Entities can access, change (variables are rewriteable)
Notes: Some built-in by Arena, you can define others. (You always define your own in AnyLogic)

## Slide 15: Pieces of a Simulation Model (cont’d.)
Resources
  What entities compete for
    People
    Equipment
    Space
  Entity seizes a resource, uses it, releases it
  Think of a resource being assigned to an entity, rather than an entity “belonging to” a resource
  “A” resource can have several units of capacity
    Seats at a table in a restaurant
    Identical ticketing agents at an airline counter
  Number of units of a resource can be changed during simulation

## Slide 16: Pieces of a Simulation Model (cont’d.)
Queues
  Place for entities to wait when they can’t move on (maybe since resource they want to seize is not available)
  Have names, often tied to a corresponding resource
  Can have a finite capacity to model limited space — have to model what to do if an entity shows up to a queue that’s already full
  It is important to track:
    Number of entities in a given queue at a given time
    Average number of entities in a given queue over time

## Slide 17: Pieces of a Simulation Model (cont’d.)
Statistical accumulators
  Variables that “watch” what’s happening
  Depend on output performance measures desired
  “Passive” components— don’t participate in model, just record
  At end of simulation, used to compute final output performance measures

## Slide 18: Pieces of a Simulation Model (cont’d.)
Statistical accumulators for simple processing system
  Number of parts produced so far
  Total waiting time spent in queue
  No. of parts that have gone through a given queue
  Max time in queue we’ve seen so far
  Total of times spent in system
  Max time in system we’ve seen so far
  Area so far under queue-length curve Q(t)
  Max of Q(t) so far
  Area so far under server-busy curve B(t)

## Slide 19: Simulation Dynamics: Event-Scheduling “World View”
Identify characteristics of events
Decide on the logic for each type of event to:
  Track state changes for each event type
  Observe statistics
  Update timings of future events (for all the entities)
Simulation clock, future event calendar
Jump from one event to the next, process, observe statistics, update event calendar
Must specify an appropriate stopping rule
Usually done with general-purpose programming language (C++, Java, Matlab, FORTRAN, etc.)

## Slide 20: Events for the Simple Processing System
Arrival of a new part to system
  Update time-persistent statistical accumulators (from last event to now)
    Area under Q(t)
    Max of Q(t)
    Area under B(t)
  “Mark” arriving part with current time
  If machine is idle:
    Start processing (schedule departure), Make machine busy, Tally waiting time in queue (0)
  Else (machine is busy):
    Put part at end of queue, increase queue-length variable
  Schedule next arrival event

## Slide 21: Events for the Simple Processing System (cont’d.)
Departure (when a service is completed)
  Increment the number-produced stat accumulator
  Compute & tally time in system (now – time of arrival)
  Update time-persistent statistics (as in arrival event)
  If queue is non-empty:
    Take the first part out of queue, compute & tally its waiting time in queue, begin service (schedule departure event)
  Else (queue is empty):
    Make machine idle (Note: there will be no departure event scheduled on future events calendar, which is as desired)

## Slide 22: Events for the Simple Processing System (cont’d.)
The End
  Update time-persistent statistics (to the end of simulation)
  Compute final output performance measures using current (= final) values of statistical accumulators
After each event, event calendar’s top record is removed to see what is the current time it, and what is next
Also must initialize everything

## Slide 23: Some Additional Specifics for the Simple Processing System
Simulation clock variable
Event calendar: list of event records:
  [Entity No., Event Time, Event Type]
  Keep ranked in increasing order based on Event Time
  Next event always in top record
  Initiate, schedule first Arrival, The End (Dep.?)
State variables: describe current status
  Server status B(t) = 1 for busy, 0 for idle
  Number of customers in queue Q(t)
  Time of arrival for each customer now in queue (a list of random length)
Notes: Clock variables are internally built in arena/anylogic

## Slide 24: Simulation by Hand
Manually track state variables, statistical accumulators
Use “given” interarrival, service times
Keep track of event calendar
“Lurch” clock from one event to next
Will omit times in system, “max” computations here (see text for complete details)

## Slide 25: Simulation by Hand: Setup

## Slide 26: Simulation by Hand: t = 0.00, Initialize

## Slide 27: Simulation by Hand: t = 0.00, Arrival of Part 1
1

## Slide 28: Simulation by Hand: t = 1.73, Arrival of Part 2
1
2

## Slide 29: Simulation by Hand: t = 2.90, Departure of Part 1
2

## Slide 30: Simulation by Hand: t = 3.08, Arrival of Part 3
2
3

## Slide 31: Simulation by Hand: t = 3.79, Arrival of Part 4
2
3
4

## Slide 32: Simulation by Hand: t = 4.41, Arrival of Part 5
2
3
4
5

## Slide 33: Simulation by Hand: t = 4.66, Departure of Part 2
3
4
5

## Slide 34: Simulation by Hand: t = 8.05, Departure of Part 3
4
5

## Slide 35: Simulation by Hand: t = 12.57, Departure of Part 4
5

## Slide 36: Simulation by Hand: t = 17.03, Departure of Part 5

## Slide 37: Simulation by Hand: t = 18.69, Arrival of Part 6
6

## Slide 38: Simulation by Hand: t = 19.39, Arrival of Part 7
6
7

## Slide 39: Simulation by Hand: t = 20.00, The End
6
7

## Slide 40: Simulation by Hand: Finishing Up
Average waiting time in queue:
Time-average number in queue:
Utilization of drill press:
= = 2.53 minutes per part

## Slide 41: Complete Record of the Hand Simulation

## Slide 42: Event-Scheduling Logic via Programming
Clearly well suited to standard programming language (C, C++, Java, etc.)
Often use “utility” libraries for:
  List processing
  Random-number generation
  Random-variate generation
  Statistics collection
  Event-list and clock management
  Summary and output
Main program ties it together, executes events in order

## Slide 43: Simulation Dynamics: Process-Interaction World View
Identify characteristic entities in system
Multiple copies of entities co-exist, interact, compete
“Code” is non-procedural
Tell a “story” about what happens to a “typical” entity
May have many types of entities, “fake” entities for things like machine breakdowns
Usually requires special simulation software
  Underneath, still executed as event-scheduling

## Slide 44: Randomness in Simulation
Above was just one “replication” — a sample of size one (not worth much)
Made a total of five replications (IID):
Confidence intervals for expected values:
  In general, (normality assumption?)
  For expected total production,
Substantial variability across replications
Precision?
Simulation: *exists*
Stochasticity:

## Slide 45: Comparing Alternatives
Usually, simulation is used for more than just a single model “configuration”
Often to compare alternatives, select or search for best (via some criterion)
Simple processing system: What would happen if arrival rate doubled?
  Cut interarrival times in half
  Rerun model for double-time arrivals
  Make five replications

## Slide 46: Results: Original vs. Double-Time Arrivals
Original – circles
Double-time – triangles
Replication 1 – filled in
Replications 2-5 – hollow
Note variability
Danger of making decisions based on one (first) replication
Hard to see if there are really differences
Need: Statistical analysis of simulation output data

## Slide 47: Simulating with Spreadsheets: Introduction
Popular, ubiquitous tool
Can use for simple simulation models
  Typically, only static models
    Risk analysis, financial/investment scenarios
  Only (very) simplest of dynamic models
Two examples
  Newsvendor problem (static)
  Waiting times in single-server queue (dynamic)
    Special recursion valid only in this case

## Slide 48: Simulating with Spreadsheets: Newsvendor Problem – Setup
Rupert sells daily newspapers on street
  Rupert buys for c = $0.55 each, sells for r = $1.00 each
Each morning, Rupert buys q copies
  q is a fixed number, same every day
Demand during a day: D = max (X, 0)
  X ~ normal (m = 135.7, s = 27.1), from historical data
  X rounds X to nearest integer
If D  q, satisfy all demand, and q – D  0 left over, sell for scrap at s = $0.03 each
If D > q, sells out (sells all q copies), no scrap
  But missed out on D – q > 0 sales
What should q be?

## Slide 49: Simulating with Spreadsheets: Newsvendor Problem – Formulation
Choose q to maximize expected profit per day
  q too small – sell out, miss $0.45 profit per paper
  q too big – have left over, scrap at a loss of $0.52 per paper
Classic operations-research problem
  Many versions, variants, extensions, applications
  Much research on exact solution in certain cases
  But easy to simulate, even in a spreadsheet
Profit in a day, as a function of q:
W(q) = r min (D, q) + s max (q – D, 0) – cq
  W(q) is a random variable – profit varies from day to day
Maximize E(W(q)) over nonnegative integers q
Sales revenue
Scrap revenue
Cost

## Slide 50: Simulating with Spreadsheets: Newsvendor Problem – Simulation
Set trial value of q, generate demand D, compute profit for that day
  Then repeat this for many days independently, average to estimate E(W(q))
    Also get confidence interval, estimate of P(loss), histogram of W(q)
  Try for a range of values of q
Need to generate demand D = max (X, 0)
  So need to generate X ~ normal (m = 135.7, s = 27.1)
  (Much) ahead – Sec. 12.2, generating random variates
  In this case, generate X = Fm,s(U)
    U is a random number distributed uniformly on [0, 1] (Sec. 12.1)
    Fm,s is cumulative distribution function of normal (m, s) distribution
1

## Slide 51: Simulating with Spreadsheets: Newsvendor Problem – Excel
File Newsvendor.xls
Input parameters in cells B4 – B8 (blue)
Trial values for q in row 2 (pink)
Day number (1, 2, ..., 30) in column D
Demands in column E for each day:
= MAX(ROUND(NORMINV(RAND(), $B$7, $B$8), 0), 0)
Rounding
function
F 1
U(0, 1)
random number
m
s
X ~ normal (m, s)
Round to nearest
integer
MAX 2nd
argument
$ pins down following column or row when copying formula
RAND() is “volatile” so regenerates on any edit, or F9 key

## Slide 52: Simulating with Spreadsheets: Newsvendor Problem – Excel (cont’d.)
For each q:
  “Sold” column: number of papers sold that day
  “Scrap” column: number of papers scrapped that day
  “Profit” column: profit (+, –, 0) that day
  Placement of “$” in formulas to facilitate copying
At bottom of “Profit” columns (green):
  Average profit over 30 days
  Half-width of 95% confidence interval on E(W(q))
    Value 2.045 is upper 0.975 critical point of t distribution with 29 d.f.
    Plot confidence intervals as “I-beams” on left edge
  Estimate of P(W(q) < 0)
    Uses COUNTIF function
Histograms of W(q) at bottom
  Vertical red line at 0, separates profits, losses

## Slide 53: Simulating with Spreadsheets: Newsvendor Problem – Results
Fine point – used same daily demands (column E) for each day, across all trial values of q
  Would have been valid to generate them independently
  Why is it better to use same demands for all q?
Results
  Best q is about 140, maybe a little less
  Randomness in all results (tap F9 key)
    All demands, profits, graphics change
    Confidence-interval, histogram plots change
    Reminder that these are random outputs, random plots
  Higher q  more variability in profit
    Histograms at bottom are wider for larger q
    Higher chance of both large profits, but higher chance of loss, too
    Risk/return tradeoff can be quantified – risk taker vs. risk-averse

## Slide 54: Simulating with Spreadsheets: Single-Server Queue – Setup
Like hand simulation, but:
  Interarrival times ~ exponential with mean 1/l = 1.6 min.
  Service times ~ uniform on [a, b] = [0.27, 2.29] min.
  Stop when 50th waiting time in queue is observed
    i.e., when 50th customer begins service, not exits system
Watch waiting times in queue WQ1, WQ2, ..., WQ50
  Important – not watching anything else, unlike before
Si = service time of customer i, Ai = interarrival time between custs. i – 1 and i
Lindley’s recursion (1952): Initialize WQ1 = 0,
WQi = max (WQi – 1 + Si – 1 – Ai, 0), i = 2, 3, ...

## Slide 55: Simulating with Spreadsheets: Single-Server Queue – Simulation
Need to generate random variates: let U ~ U[0, 1]
  Exponential (mean 1/l): Ai = –(1/l) ln(1 – U)
  Uniform on [a, b]: Si = a + (b – a) U
File MU1.xls
Input parameters in cells B4 – B6 (blue)
  Some theoretical outputs in cells B8 – B10
Customer number (i = 1, 2, ..., 50) in column D
Five IID replications (three columns for each)
  IA = interarrival times, S = service times
  WQ = waiting times in queue (plot, thin curves)
    First one initialized to 0, remainder use Lindley’s recursion
      Curves rise from 0, variation increases toward right
    Creates positive autocorrelation down WQ columns
      Curves have less abrupt jumps than if WQi’s were independent

## Slide 56: Simulating with Spreadsheets: Single-Server Queue – Results
Column averages (green)
  Average interarrival, service times close to expectations
  Average WQi within each replication
    Not too far from steady-state expectation
    Considerable variation
    Many are below it (why?)
Cross-replication (by customer) averages (green)
  Column T, thick line in plot to dampen noise
Why no sample variance, histograms of WQi’s?
  Could have computed both, as in newsvendor; two issues:
    Nonstationarity – what is a “typical” WQi here?
    Autocorrelation – biases variance estimate, may bias histogram if run is not “long enough”

## Slide 57: Simulating with Spreadsheets: Recap
Popular for static models
  Add-ins – @RISK, Crystal Ball
Inadequate tool for dynamic simulations if there’s any complexity
  Extremely easy to simulate single-server queue in Arena – Chapter 3 main example
  Can build very complex dynamic models with Arena – most of rest of book

## Slide 58: Overview of a Simulation Study
Understand system
Be clear about goals
Formulate model representation
Translate into modeling software
Verify “program”
Validate model
Design experiments
Make runs
Analyze, get insight, document results