## Slide 1: Random Number/variable generation
Industrial & Systems Engineering
University of Tennessee, Knoxville
Xueping Li

## Slide 2: Let’s try to get some “random” numbers
2,4;
1,2;
1,3;
3,4;
5,7;
5,8;
1,3;
3,8

## Slide 4: Monte Carlo methods
“Monte Carlo methods (or Monte Carlo experiments) are a broad class of computational algorithms that rely on repeated random sampling to obtain numerical results. They are often used in physical and mathematical problems and are most useful when it is difficult or impossible to use other mathematical methods. Monte Carlo methods are mainly used in three distinct problem classes: optimization, numerical integration, and generating draws from a probability distribution.”
Courtesy of Wikipedia

## Slide 6: RNGs
Random Numbers Generators
  Mid-square method
  LCM (LCG)
  …

## Slide 7: Random Numbers
Why is random number generation necessary?
  In a simulated system, there are inherently random components that require a method of obtaining numbers that are random.
  For example - a queuing system model requires interarrival times, service times, etc., that were drawn from some specified distribution.

## Slide 8: Properties of Random Numbers
Two important statistical properties:
  Uniformity
  Independence.
Random Number, Ri, must be independently drawn from a uniform distribution with pdf:
Figure: pdf for random numbers

## Slide 9: Cont.
Independence - the probability of observing a value in a particular interval is independent of the previous value drawn.
Expected value and variance of random numbers
  Expected value of each Ri is given by
  Variance for each Ri is given by

## Slide 10: Generation of Pseudo-Random Numbers
“Pseudo”, because generating numbers using a known method removes the potential for true randomness.
Goal: To produce a sequence of numbers in [0,1] that simulates, or imitates, the ideal properties of random numbers (RN).
Important considerations in RN routines:
  Fast
  Portable to different computers
  Have sufficiently long cycle
  Replicable
  Closely approximate the ideal statistical properties of uniformity and independence.

## Slide 11: Midsquare Generator
Random number seed - initial random number used to generate the next random number which is in turn transformed into the new seed value.
Proposed by von Neumann and Metropolis in the 1940’s
  Start with an initial four-digit positive integer seed X0
  Square it to obtain an integer with up to eight digits
  Take the middle four digits as the next four-digit number, X1
  Place a decimal point at the left of X1 to get first random number R1
  Square X1 and continue process

## Slide 12: Example
Let X0 = 5497
X1 = (5497)2 = 30217009 X1 = 2170, R1 = 0.2170
X2 = (2170)2 = 04708900 X2 = 7089, R2 = 0.7089
X3 = (7089)2 = 50253921 X3 = 2539, R3 = 0.2539
...and so on...
Pros of the midsquare method
  Rather simple to implement
Cons of the midsquare method
  Difficult to choose initial seed that will give good sequence
  Strong tendency to degenerate fairly rapidly to zero

## Slide 13: More examples (poor)
Let X0 = 5197
X1 = (5197)2 = 27008809 X1 = 0088, R1 = 0.0088
X2 = (0088)2 = 00007744 X2 = 0077, R2 = 0.0077
X3 = (0077)2 = 00005929 X3 = 0059, R3 = 0.0059
X4 = (0059)2 = 00003481 X4 = 0034, R4 = 0.0034
Let X0 = 6500
X1 = (6500)2 = 42250000 X1 = 2500, R1 = 0.2500
X2 = (2500)2 = 06250000 X2 = 2500, R2 = 0.2500

## Slide 14: More examples …

## Slide 15: Linear Congruential Generator
To produce a sequence of integers, X1, X2, … between 0 and m-1 by following a recursive relationship:
X(i+1)=(a*X(i) +C) mod m
The selection of the values for a, c, m, and X0 drastically affects the statistical properties and the cycle length.
The random integers are being generated [0,m-1], and to convert the integers to random numbers:

## Slide 16: E.g.,
Use X0 = 27, a = 17, c = 43, and m = 100.
The Xi and Ri values are:
  X1 = (17*27+43) mod 100 = 502 mod 100 = 2, R1 = 0.02;
  X2 = (17*2+43) mod 100 = 77, R2 = 0.77;
  X3 = (17*77+43) mod 100 = 52, R3 = 0.52;
  …

## Slide 17
Period = 2000

## Slide 18: LCG:: “Good” Examples
A= 25214903917, M=2^48, C=11
A=6364136223846793005, M=2^64, C=1442695040888963407

## Slide 24: Characteristics of a Good Generator
Maximum Density
  Such that he values assumed by Ri, i = 1,2,…, leave no large gaps on [0,1]
  Problem: Instead of continuous, each Ri is discrete
  Solution: a very large integer for modulus m
    Approximation appears to be of little consequence
Maximum Period
  To achieve maximum density and avoid cycling.
  Achieve by: proper choice of a, c, m, and X0.
Most digital computers use a binary representation of numbers
  Speed and efficiency are aided by a modulus, m, to be (or close to) a power of 2.

## Slide 25: Other Generators
Quadratic Congruential Generator
  Xnew = (a1 * Xold2 + a2 * Xold + c) mod m
Combination of generators
  Shuffling – shuffle the output from the first LCG with a second LCG
  L’Ecuyer – takes integers generated from two different LCGs with different moduli, then
  Wichman/Hill – takes the fractional parts of multiple random numbers generated from separate generators
Trausworthe generator
  Generates sequence of random bits

## Slide 26: Combined Linear Congruential Generators
Example: For 32-bit computers, L’Ecuyer [1988] suggests combining k = 2 generators with m1 = 2,147,483,563, a1 = 40,014, m2 = 2,147,483,399 and a2 = 20,692. The algorithm becomes:
  Step 1: Select seeds
    X1,0 in the range [1, 2,147,483,562] for the 1st generator
    X2,0 in the range [1, 2,147,483,398] for the 2nd generator.
    Step 2: For each individual generator,
    X1,j+1 = 40,014 X1,j mod 2,147,483,563
    X2,j+1 = 40,692 X1,j mod 2,147,483,399.
  Step 3: Xj+1 = (X1,j+1 - X2,j+1 ) mod 2,147,483,562.
  Step 4: Return
  Step 5: Set j = j+1, go back to step 2.
  Combined generator has period: (m1 – 1)(m2 – 1)/2 ~ 2 x 1018

## Slide 27: Tests for Random Numbers
Two categories:
  Testing for uniformity:
  H0: Ri ~ U[0,1]
  H1: Ri ~ U[0,1]
    Failure to reject the null hypothesis, H0, means that evidence of non-uniformity has not been detected.
  Testing for independence:
  H0: Ri ~ independently
  H1: Ri ~ independently
    Failure to reject the null hypothesis, H0, means that evidence of dependence has not been detected.
Level of significance a, the probability of rejecting H0 when it is true: a = P(reject H0|H0 is true)

## Slide 28: Frequency Tests
Test of uniformity
Two different methods:
  Kolmogorov-Smirnov test
  Chi-square test

## Slide 29: Kolmogorov-Smirnov Test
Compares the continuous cdf, F(x), of the uniform distribution with the empirical cdf, SN(x), of the N sample observations.
  We know:
  If the sample from the RN generator is R1, R2, …, RN, then the empirical cdf, SN(x) is:
Based on the statistic: D = max| F(x) - SN(x)|
  Sampling distribution of D is known (a function of N, tabulated in Table A.8.)
A more powerful test, recommended.

## Slide 30
30
Kolmogorov-Smirnov Test
Example: Suppose 5 generated numbers are 0.44, 0.81, 0.14, 0.05, 0.93.
Step 1:
Step 2:
Step 3: D = max(D+, D-) = 0.26
Step 4: For a = 0.05,
Da = 0.565 > D
Hence, H0 is not rejected.
Arrange R(i) from smallest to largest
D+ = max {i/N – R(i)}
D- = max {R(i) - (i-1)/N}
R(i) | 0.05 | 0.14 | 0.44 | 0.81 | 0.93
i/N | 0.20 | 0.40 | 0.60 | 0.80 | 1.00
i/N – R(i) | 0.15 | 0.26 | 0.16 | - | 0.07
R(i) – (i-1)/N | 0.05 | - | 0.04 | 0.21 | 0.13

## Slide 32
Chi-square test uses the sample statistic:
  Approximately the chi-square distribution with n-1 degrees of freedom (where the critical values are tabulated in Table A.6)
  For the uniform distribution, Ei, the expected number in the each class is:
Valid only for large samples, e.g. N >= 50
n is the # of classes
Oi is the observed # in the ith class
Ei is the expected # in the ith class

## Slide 33: Using R to run KS-test?

## Slide 34: Random-Variate Generation
Purpose
  Develop understanding of generating samples from a specified distribution as input to a simulation model.
  Illustrate some widely-used techniques for generating random variates.
    Inverse-transform technique
    Acceptance-rejection technique
    Special properties

## Slide 35: Inverse-transform Technique
The concept:
  For cdf function: r = F(x)
  Generate r from uniform (0,1)
  Find x:
r1
x1
r = F(x)
x = F-1(r)

## Slide 36: Exponential Distribution
Exponential Distribution:
  Exponential cdf:
  To generate X1, X2, X3 …
r = F(x)
= 1 – e-lx for x ³ 0
Xi = F-1(Ri)
= -(1/l) ln(1-Ri)
Figure: Inverse-transform technique for exp(l = 1)

## Slide 37: Non-stationary Poisson Process (NSPP)
A Poisson arrival process with an arrival rate that varies with time
Procedures:
Step 1. l* = max l(t) = 1/5, t = 0 and i = 1.
Step 2. For random number R = 0.2130,
E = -5ln(0.213) = 13.13
t = 13.13
Step 3. Generate R = 0.8830
l(13.13)/l*=(1/15)/(1/5)=1/3
Since R>1/3, do not generate the arrival
Step 2. For random number R = 0.5530,
E = -5ln(0.553) = 2.96
t = 13.13 + 2.96 = 16.09
Step 3. Generate R = 0.0240
l(16.09)/l*=(1/15)/(1/5)=1/3
Since R<1/3, T1 = t = 16.09,
and i = i + 1 = 2

## Slide 39: Generate random numbers in R
>runif()

## Slide 40: Using the R generators

## Slide 41: Uniform simulation

## Slide 42: Checking the generator

## Slide 43: Cont.

## Slide 44: Cont.

## Slide 45: The Inverse Transformation

## Slide 46: Exponential

## Slide 47: Using uniform

## Slide 48: General Transformation Methods

## Slide 49: Example

## Slide 50: Caveats

## Slide 51: A Normal Generator

## Slide 53: Discrete Distributions

## Slide 54: Binomial
Notes: > ppois(0,7)
[1] 0.000911882
> ppois(1,7)
[1] 0.007295056

## Slide 55
n=10;p=.3;nsim=1000
prob=pbinom(c(0:n),n,p)
X=array(0,dim=c(nsim,1))
for(i in 1:nsim){X[i]=sum(runif(1)>prob)
hist(X,freq=F)
lines(c(0:n)-.5,dbinom(c(0:n),n,p))}

## Slide 56: Cont. comments

## Slide 57: Poisson

## Slide 58
Nsim=10^4; lambda=100
spread=3*sqrt(lambda)
t=round(seq(max(0,lambda-spread),lambda+spread,1))
prob=ppois(t, lambda)
X=rep(0,Nsim)
for (i in 1:Nsim){u=runif(1);X[i]=t[1]+sum(prob<u)-1 }
hist(X)

## Slide 59: Cont.

## Slide 61: Mixture distribution

## Slide 62: Cont.

## Slide 64: Generating the mixture

## Slide 65
p1<-.15; p2=.5;p3=1-p1-p2;p=c(p1,p2,p3)
m=c(-3,0,2);s=c(1,1,.75)
nsim<-50000;X=array(0,c(nsim,1))
for(i in 1:nsim){j=sum(runif(1)>cumsum(p));X[i]=rnorm(1,mean=m[j+1],sd=s[j+1])}
#This plots histogram and density#
hist(X,freq=F,col="gray",breaks=50)
xplot=seq(min(X),max(X),.1)
Mix=function(x){p[1]*dnorm(x,m[1],s[1])+p[2]*dnorm(x,m[2],s[2])+p[3]*dnorm(x,m[3],s[3])}
lines(xplot,Mix(xplot),lwd=2)

## Slide 66: Continuous mixtures

## Slide 68: Accept-Reject Methods

## Slide 69: Accept-Reject Algorithm

## Slide 70: R implementation

## Slide 71: Normal & Double Exponentials
Notes: f=function(x){-x^2/2+x}
optimize(f,interval=c(0,10), maximum=TRUE)

## Slide 72: Code
par(mfrow=c(1,2))
nsim=10000
Y=rexp(nsim)
for(i in 1:nsim) if(runif(1)<.5) Y[i]=-Y[i]#random sign
hist(Y,freq=F,col="gray",breaks=50)
for(i in 1:nsim) Y[i]=Y[i]*(runif(1)<exp(-.5*Y[i]^2+abs(Y[i])-.5))
Y<-Y[Y!=0] #eliminate zeros
length(Y)/nsim #percent accepted
hist(Y,freq=F,col="red",breaks=50)
yplot=seq(min(Y),max(Y),.1)
lines(yplot, dnorm(yplot), lwd=2)

## Slide 73: Theory

## Slide 74: Beta from Uniform

## Slide 75: Code
par(mfrow=c(1,2))
nsim<-10000
a<-2.7; b<-6.3; #Target
a1=1; b1=1 #Candidate
temp=(a-a1)/(a-a1+b-b1)
M=(temp^(a-a1))*((1-temp)^(b-b1))
Y=rbeta(nsim,a1,b1)
hist(Y,freq=F,col="gray",breaks=50)
for(i in 1:nsim) Y[i]=Y[i]*(runif(1)<(Y[i]^(a-a1))*((1-Y[i])^(b-b1))/M)
Y<-Y[Y!=0] #eliminate zeros
length(Y)/nsim #percent accepted
hist(Y,freq=F,col="red",breaks=50)
yplot=seq(min(Y),max(Y),.01)
lines(yplot, dbeta(yplot,a,b), lwd=2)

## Slide 76: Beta from Beta

## Slide 78: Comments

## Slide 79: R code
RNG.R

## Slide 80: What’s next?
MCMC
A tour of AnyLogic

## Slide 81: Acknowledgement
Wikipedia.Org
Christian P. Robert & George Casella, “Introducing Monte Carlo Methods with R”. Springer, 2009.