## Slide 1: Fundamental Simulation Concepts
Mohammad Ramshani
University of Tennessee

## Slide 2: What We’ll Do ...
Underlying ideas, methods, and issues in simulation
Software-independent (setting up for AnyLogic)
Example of a simple processing system
  Scope the problem
  Terminology
  Simulation by hand
  Some basic statistics
Spreadsheet simulation
  Simple static/dynamic models
Overview of a simulation study

## Slide 3: The System: A Simple Processing System
Arriving
Blank Parts
Departing
Finished Parts
Machine
(Server)
Queue (FIFO)
Part in Service
4
5
6
7
General intent:
  Estimate expected production
  Waiting time in queue, queue length, utilization of the machine (the proportion of time the machine is busy)
Time units
  Different units in different places … must declare
  Check units when specifying inputs
  Declare base time units for internal calculations, outputs
  Be reasonable (interpretation, roundoff error)

## Slide 4: Model Specifics
Initially (time 0) empty and idle
Base time units: minutes
Input data (assume given for now) in minutes:
Part Number Arrival Time Interarrival Time Service Time
1 0.00 1.73 2.90
2 1.73 1.35 1.76
3 3.08 0.71 3.39
4 3.79 0.62 4.52
5 4.41 14.28 4.46
6 18.69 0.70 4.36
7 19.39 15.52 2.07
8 34.91 3.15 3.36
9 38.06 1.76 2.37
10 39.82 1.00 5.38
11 40.82 . .
. . . .
. . . .
Stop when 20 minutes of (simulated) time have passed
Notes: Production within 20 minutes = 5 parts; / 5
Average Waiting Time in Queue = 2.49 mins /

## Slide 5: Goals of Study: Output Performance Measures
Total production of parts per run (P)
Average waiting time of parts in queue:
Maximum waiting time for parts in queue:
= no. of parts which left the queue
= waiting time in queue of part
Question:
  WQ1 =
  N >
0
?
?
1

## Slide 6: Goals of Study: Output Performance Measures (cont’d.)
Average number of parts in queue over time:
Maximum number of parts in queue:
Average and maximum total time in system (a.k.a. cycle time):
Q(t) = number of parts in queue
at time t
TSi = time in system of part i

## Slide 7: Goals of Study: Output Performance Measures (cont’d.)
Utilization of machine (proportion of time busy)
Such measures are referred to as Key Performance Indicators (KPIs)

## Slide 8: Analysis Options
Educated guessing
  Average interarrival time = 4.08 minutes
  Average service time = 3.46 minutes
  So (on average) parts are being processed faster than they arrive
    System has a chance of operating in a stable way in long run, i.e., might not “explode”
    If all interarrivals and service times were exactly at their mean, there would never be a queue
    But data clearly exhibit variability, so a queue could form
  If we’d had average interarrival < average service time, and this persisted, then queue would explode
  Truth — between these extremes
  Guessing has its limits …

## Slide 9: Analysis Options (cont’d.)
Queueing theory
  Requires additional assumptions about model
  Popular, simple model: M/M/1 queue
    Interarrival times ~ exponential (what is the distribution of arrival times?)
    Service times ~ exponential, indep. of interarrivals
    Must have E(service) < E(interarrival)
    Steady-state (long-run, forever)
    Exact analytic results; e.g., average waiting time in queue is
  Problems: validity, estimating means, time frame
  But it’s all about approximation!
Notes: M/M/1 queue represents the queue length in a system having a single server, where arrivals are determined by a Poisson process and job service times have an exponential distribution.
the M stands for Markovian; M/M/1 means that the system has a Poisson arrival process

## Slide 10: Poison Distribution
Often the arrival process of customers can be described by a Poisson process
  Poisson process is a pure birth process
  The number of arrivals N(t) in a finite interval of length t obeys the Poisson(λt) distribution
  The interarrival times are independent and obey the Exp(λ) distribution
Notes: Pure birth process = it basically means that we only go from state n to state n+1 (mu = 0 or no death or backward transition happens so we do not go from n to n-1)
1- In an infinitesimal time interval dt there may occur only one arrival. This happens with the probability λdt independent of arrivals outside the interval.
2- Moreover, the number of arrivals N(t1, t2) and N(t3, t4) in non-overlapping intervals (t1 ≤ t2 ≤ t3 ≤ t4) are independent.

## Slide 11: Mechanistic Simulation
Individual operations (arrivals, service times) will occur exactly as in reality
Movements, changes occur at right “times,” in right order
Different pieces interact
Install “observers” to get output performance measures
Concrete, “brute-force” analysis approach
Nothing mysterious or subtle
  But a lot of details, bookkeeping
  Simulation software keeps track of things for you
What is brute-force approach?
Notes: Mechanistic: We can understand the system by studying it’s underlaying parts and their relations
Brute-force: you go through all possible scenarios and enumerate them.

## Slide 12: Pieces of a Simulation Model
Entities
  “Players” that move around, change status, affect and are affected by other entities
  Dynamic objects — created, processed, removed (maybe)
  Usually represent “real” objects/beings
    Examples: parts in a factory, pizza in a pizzeria, drinks in a bar
    Can have “fake” entities for modeling “tricks”
  Usually have multiple realizations floating around
  Can have different types of entities concurrently
  Usually, identifying types of entities is first thing to do in building model

## Slide 13: Pieces of a Simulation Model (cont’d.)
Attributes
  Characteristic of all entities: describe, differentiate
  All entities have same attribute “slots” but different values for different entities, for example:
    Time of arrival
    Due date
    Priority
    Color
  Attribute value tied to a specific entity
  Like “local” (to entities) variables

## Slide 14: Pieces of a Simulation Model (cont’d.)
(Global) Variables
  Reflect characteristics of the whole model, not of specific entities, i.e.,
    Values for which there’s only one copy for the whole model
  Example:
    Travel time between all station pairs
    Number of parts in system
    Simulation clock
  Not tied to entities
  Entities can access, change (variables are rewriteable)
Notes: Some built-in by Arena, you can define others. (You always define your own in AnyLogic)

## Slide 15: Pieces of a Simulation Model (cont’d.)
Resources
  What entities compete for
    People
    Equipment
    Space
  Entity seizes a resource, uses it, releases it
  Think of a resource being assigned to an entity, rather than an entity “belonging to” a resource
  “A” resource can have several units of capacity
    Seats at a table in a restaurant
    Identical ticketing agents at an airline counter
  Number of units of a resource can be changed during simulation

## Slide 16: Pieces of a Simulation Model (cont’d.)
Queues
  Place for entities to wait when they can’t move on (maybe since resource they want to seize is not available)
  Have names, often tied to a corresponding resource
  Can have a finite capacity to model limited space — have to model what to do if an entity shows up to a queue that’s already full
  It is important to track:
    Number of entities in a given queue at a given time
    Average number of entities in a given queue over time
Notes: It’s important to calculate these KPIs so we can find where the bottleneck is, mainly to evaluate other scenarios.

## Slide 17: Pieces of a Simulation Model (cont’d.)
Statistical accumulators
  Variables that “watch” what’s happening
  Depend on output performance measures desired
  “Passive” components— don’t participate in model, just record
  At end of simulation, used to compute final output performance measures

## Slide 18: Pieces of a Simulation Model (cont’d.)
Statistical accumulators for simple processing system
  Number of parts produced so far
  Total waiting time spent in queue
  No. of parts that have gone through a given queue
  Max time in queue we’ve seen so far
  Total time (spent) in system
  Max time in system we’ve seen so far
  Area so far under queue-length curve Q(t)
  Max of Q(t) so far
  Area so far under server-busy curve B(t)
Notes: number of parts in queue at time t

## Slide 19: Example
Ordering pizza
  What are the resources?
  What are the entities?
    What are their attributes?
  What are the variables?

## Slide 20: Simulation Dynamics: Event-Scheduling “World View”
Identify characteristics of events
Decide on the logic for each type of event to:
  Track state changes for each event type
  Observe statistics
  Update timings of future events (for all the entities)
Simulation clock, future event calendar
Jump from one event to the next, process, observe statistics, update event calendar
Must specify an appropriate stopping rule
Usually done with general-purpose programming language (C++, Java, Matlab, FORTRAN, etc.)

## Slide 21: Events for the Simple Processing System
Arrival of a new part to system
  Update time-persistent statistical accumulators (from last event to now)
    Area under Q(t)
    Max of Q(t)
    Area under B(t)
  “Mark” arriving part with current time
  If machine is idle:
    Start processing (schedule departure), Make machine busy, Calculate waiting time in queue (0)
  Else (machine is busy):
    Put part at end of queue, increase queue-length variable
  Schedule next arrival event

## Slide 22: Events for the Simple Processing System (cont’d.)
Departure (when a service is completed)
  Increment the number-produced stat accumulator
  Compute time in system (now – time of arrival)
  Update time-persistent statistics (as in arrival event)
  If queue is non-empty:
    Take the first part out of queue, compute its waiting time in queue, begin service (schedule departure event)
  Else (queue is empty):
    Make machine idle (Note: there will be no departure event scheduled on future events calendar)

## Slide 23: Events for the Simple Processing System (cont’d.)
The End
  Update time-persistent statistics (to the end of simulation)
  Compute final output performance measures using current (= final) values of statistical accumulators
After each event, event calendar’s top record is removed to see what is the current time, and what is next

## Slide 24: Some Additional Specifics for the Simple Processing System
Simulation clock variable
Event calendar: list of event records:
  [Entity No., Event Time, Event Type]
  Keep ranked in increasing order based on Event Time
  Next event always in top record
  Initiate, schedule first Arrival, The End (Dep.?)
State variables: describe current status
  Server status B(t) = 1 for busy, 0 for idle
  Number of customers in queue Q(t)
  Time of arrival for each customer now in queue (a list of random length)
Notes: Clock variables are internally built in arena/anylogic